## Slide 2: Into - toby

## Slide 3: BOARD - ED

## Slide 4: TRUCKS - TOBY

## Slide 5: Wheels - HUGO

## Slide 6: Battery – SAM

## Slide 7: Range specification
Specification
Charge every week: 7 days
Days in use: 5 days (commute)
Distance each day: 3km
Estimated vertical distance: 80m
This means:
Estimated Watt-hours per mile: 10Wh/mile

## Slide 8: Battery specification
Lithium polymer chemistry
Watt-hour capacity: 180Wh
Supply voltage:22.2V
Amp-hour capacity: 8100Ah
Mass: 1.7kg
Supply voltage: 50v
2 batteries in parallel required

## Slide 9: Battery charging
Lithium polymer can be dangerous:
  Overcharging
  Unbalanced charging
Use an off the shelf solution
Use hobby/RC charger
Charge batteries in parallel
System to switch between series and parallel

## Slide 10: Battery control overview

## Slide 11: Battery embedded controller
STM8L – microcontroller
Ultra low power 10 sleep state
Separate battery supply
Monitors battery health
  Volts
  Time
  Cycle count
Controls battery mux
Controls charge circuit
Heartbeat signal from main micro

## Slide 12: Battery error state
LED binary error code report
Flashes on when power button is hit
Lookup table in manual

## Slide 13: Battery mux
Two large batteries
States:
  Charge in parallel
  Discharge in series
Electrically controlled path switching
Vibration resistant
Short resistant
Bidirectional current flow (balanced charging)

## Slide 14: Switching technology
Relay:
Mechanical switch
Very High voltage
Very High current
Low standby draw
Bipolar power switch(BPS):
Solid state system
MOSFET switching
Higher power dissipation
Fast switching